Using Digilinet Nexys3 for control and DUT

This document describes how to use Nexys3 as a controller and DUT.

High level diagram for FOBOS boards. The din and dout buses are 4 bit each.

Controller

PMOD connector pin assignment on the control board.

PORT A	PORT B	PORT C	PORT D
JA1:	JB1: EXTClock (from clk Generator)	JC1: DUTClock	JD1: reset
JA2:	JB2:	JC2: do_ready	JD2: di_ready
JA3: trigger (to osciloscope)	JB3:	JC3: din(3)	JD3: dout(3)
JA4:	JB4:	JC4: din(1)	JD4: dout(1)
JA7:	JB7:	JC7: do_valid	JD7:
JA8:	JB8:	JC8:	JD8: di_valid
JA9:	JB9:	JC9: din(2)	JD9: dout(2)
JA10:	JB10:	JC10: din(0)	JD10: dout(0)

PMOD connector pin assignment on the DUT board.

PORT A	PORT B	PORT C	PORT D
JA1:	JB1:	JC1: DUTClock	JD1: reset
JA2:	JB2:	JC2: do_ready	JD2: di_ready
JA3: trigger	JB3:	JC3: din(3)	JD3: dout(3)
JA4:	JB4:	JC4: din(1)	JD4: dout(1)
JA7:	JB7:	JC7: do_valid	JD7:
JA8:	JB8:	JC8:	JD8: di_valid
JA9:	JB9:	JC9: din(2)	JD9: dout(2)
JA10:	JB10:	JC10: din(0)	JD10: dout(0)

Note that the two boards must share GND. PMOD ports C and D are connected, each pin to its corresponding pin in the other board (e.g. JA1 -> JA1 and GND-> GND). However the 3.3 V pin is not connected in the PMOD connector.